## Slide 1: Border Gateway Protocol
COSC 650 - Fall 2014

## Slide 2: Dr. Alexander L. Wijesinha
Ibtihaj Alanazi
Logan Bair
Amirshahram Hematian
Kevin Kuo
Mary Snyder

## Slide 3: Topics
Overview/Introduction
  Popularity and Use of BGP in Information Technology Applications
  Advantages and Disadvantages of BGP
Reasons for Implementation
  Best Bath Selection Algorithm
Implementation of Standard
  Message Format
  Routing Updates
  Path Attributes
  Error Handling
  Version Negotiation
  Timers
  Security
Hardware and Software Requirements
Vulnerabilities of BGP

## Slide 4: Border Gateway Protocol (BGP)
BGP is a widely used routing protocol to route traffic among gateway hosts in a network of autonomous systems (ASs).
BGP uses Transmission Control Protocol (TCP) to communicate between hosts.
BGP routing decision are made using the Best Path Selection, which utilizes known routes/paths and network policies to determine routes free of loops.
BGP only sends updated routing information when changes occur and transmits only the updated information.
BGP-4 is the latest version which allows network administrators to configure the routes according to organizational policy statements.

## Slide 5: Popularity and Use of BGP in Information Technology Applications
BGP is popular among network administrators of multiple ISPs or single ISPs with a need to connect with other network providers.
BGP can be used to join a number of Open Shortest Path First (OSPF) networks.
BGP is also used by may large private IP networks internally where OSPF by itself would not scale
BGP is important in multi-homing networks, creating a reliable connections that give better redundancy instead of multiple access points.

## Slide 6: Advantages and Disadvantages of BGP
Advantages
  Only one active route for a prefix at a time
  Ensures the decision process between multiple routes does not cause loops.
  Blocks source of bad traffic
  Provides IP stability
Disadvantages
  Found to be vulnerable to attacks and misconfigurations.
  Congestion control/monitoring is not performed
  Inability to load balance traffic across multiple connections during high load

## Slide 7: Reasons for Implementation
  The primary function of a BGP speaker is to exchange network reachability information with other BGP systems.
  This is accomplished through use of the Best Path Selection Algorithm
    Reducing routing and forwarding changes in a network, creating a more stable network
    Quickly identifying and removing any routing loops
    Enforcing policy decisions

## Slide 8: Best Path Selection Algorithm
Prefer the route with highest WEIGHT [Cisco-specific, local to the router].
Prefer the route with highest LOCAL_PERF [Local within an AS].
Prefer locally originated routes.
Prefer the route with the shortest AS_PATH.
Prefer the route with lowest origin code (i.e. In order of preference: IGP, EGP, incomplete routes).
Prefer the route with the lowest multi-exit discriminator (MED).
Prefer EBGP learnt routes over IBGP learnt routes. If best route is selected, skip next step
Prefer the route with the smallest IGP metric to the BGP next-hop.
Determine if multiple routes require installation into the routing table for BGP Multipath. If best route is not selected, continue to next step
When both routes are external, prefer the oldest route (received first)
Prefer the route from the BGP router with the lowest router ID.
When both router IDs are the same for multiple routes, prefer the route with the smallest cluster list.
Prefer the route with the lowest neighbor address.

## Slide 9: Implementation of Standard
  Message Format
    Max size 4096 bytes; Smallest size 19 bytes (header and no data)
    All fields are multi-byte fields are big-endian
    4 types of BGP messages: Open, Update, Notification, and Keep Alive.
  Routing Updates
    Entire routing table is sent when a peer/speaker boots
    After boot only updates are sent
    Route updates are stored in the Routing Information Base (RIB)
  Path Attributes
    AS_PATH – path that traverses the least number of AS.
    MED – allows an exit point to be specified to a remote AS for a multi exit point network.
    Origin – specifies the origin of a routing update; can be used in determining the preferred route
  Error Handling
    When an error occurs, a notification message with the following is sent:
      Error Code
      Error Subcode (0 if none specified)
      Data fields
    Routing table entries errors associated with remote BGP speakers are marked as invalid

## Slide 10: Implementation of Standard (cont.)
  Version Negotiation
    Negotiated by making multiple attempts at opening a BGP connection, starting with the highest number the BGP speaker supports
    Highest common version between BGP speakers is used
  Timers
    BGP employs five main timers and two optional timers:
      ConnectRetryTimer (default 120 seconds)
      HoldTimer (default 90 seconds)
      KeepaliveTimer (default 1/3 HoldTimer)
      MinASOriginationIntervalTimer (default 15 seconds)
      MinRouteAdvertisementIntervalTimer (default 30 seconds for EBGP; 5 seconds for IBGP)
      Optional: DelayOpenTimer
      Optional: IdleHoldTimer
  Security
    Uses TCP for reliability of traffic transport between BGP speakers with added mechanisms defined in RFC 2385 to:
      Detect and reject wiretapping attacks
      Augments the normal TCP checksum with a 16-byte message authentication code (MAC) based on MD5

## Slide 11: Hardware and Software Requirements for BGP
Routers usually used in small offices and/or home networks may not be capable of running BGP.
Commercial grade routers found in large enterprise networks and Internet Service Providers (ISPs) typically have operating systems that are capable of supporting BGP.
  Common manufacturers include Cisco, Alcatel Lucent, and Juniper Networks.
The actual amount of memory required for a BGP speaker depends on the volume of BGP information exchanged with the other BGP speakers as well as the way the particular BGP speaker stores BGP information.
Open source packages capable of running BGP include GNU Zebra, Ouagga, Open BGPD, BIRD, XORP, and Vyatta.

## Slide 12: Vulnerabilities of BGP
Confidentiality violations (eavesdropping)
Replay
Message Insertion
  Since BGP uses TCP, this is much more difficult after the TCP connection has been completely established
Message Deletion
  Again this is much more difficult, but not impossible, once the TCP connection has been completely established
Message Modification
  Any modification that maintains the syntax and length of the TCP payload may not be detected
Man-in-the-Middle
  BGP does not perform any authentication for BGP speakers/peers.
Denial of Service (DoS)
  The most critical DoS attack would be one on the BGP routing protocol itself.